## Slide 1
CS 3630!
Lecture 3:
A Trash Sorting Robot:
states and actions

## Slide 2: Lecture 2 Recap

## Slide 3: A Taxonomy of Robotics Topics
For each module in this class, we’ll consider six distinct aspects of robotics:
State: How does the robot represent its world, and itself?
Actions: What can the robot do, and how to represent this?
Sensors: What information about the world can be ascertained via sensing, and how do we model this process?
Perception: How can we combine sensor data with contextual knowledge to understand the current state?
Planning: What actions should the robot execute to transform the state of the world into a desired goal state?
Learning: How can the robot improve its knowledge over time, using information that it acquires during operation?
Each chapter of the book includes six sections, corresponding to these topics.

## Slide 4: Robots in the real world
For specific applications, these topics correspond to specific problems that robots must solve to operate effectively.
For example, a museum guide robot might need to solve the following problems:
State: where is the robot, and where are the humans to be guided?
Actions: move from room to room
Sensors: cameras
Perception: use computer vision to understand human intention, and to localize
Planning: what path to take in order to guide humans to their desired exhibit
Learning: which parts of the museum are crowded, and when to avoid these?

## Slide 5: How do robots function in the world
When they are deployed in the world, most robots use the so-called Sense-Think-Act paradigm of operation.
This can be viewed as an overall control structure, in which state, actions, sensors, perception, planning, and learning play specific roles.

## Slide 6
Real-world Environment
Perception
Localization
Planning
Motion Control
Environment model, Local map
Position, Global map
Path
Path Execution
Example: Navigation in a Known Environment
ACT
THINK
SENSE
In most robotics applications, the robot does not succeed to perform the task using a single episode of sense, think, act.
Typically, these stages are repeated until the task is achieved: the sense, think, act loop.

## Slide 7
Sense, Think, Act at Different Time Scales
SENSE
THINK
ACT
Cycle time
The time to complete one cycle of this loop depends on the task:
Playing chess: minutes
Hand-eye coordination: 30 Hz
Force controlled robot: Order of KHz
When cycle time is very fast, we use tools from control theory, and model systems using differential equations (continuous time performance).
When cycle time is very slow, we might have scene understanding and deliberative planning.
As computers become faster, the boundary between these begins to blur.

## Slide 8: A Trash Sorting Robot Chapter 2

## Slide 9: A Trash Sorting Robot
Our first example is a trash sorting robot.
Individual pieces of trash arrive to the robot’s work cell on a conveyor belt.
The robot’s task is to place each piece of trash in an appropriate bin:
Glass
Mixed paper
Metal
Nop
Sensors measure various characteristics of the trash, which are used to make inferences about the object type (perception).
We assume sensor uncertainty, but perfect execution of actions.
Over time, sensor models can be refined using machine learning methods.

## Slide 10: Modeling the World State
For this problem, the only interesting aspect of the world state is the specific material composition of the item of trash that is currently in the robot’s work cell.
We consider five possibilities:
Cardboard
Paper
Cans
Scrap Metal
Bottles
For this chapter, we assume that there are no other possibilities.
You should probably just memorize these now, because they’re going to be used a lot in this chapter.

## Slide 11: Modeling Uncertainty
We assume that there is uncertainty in sensing, and therefore, it is not possible to know with certainty the world state.
We consider the state to be a random quantity, with five possible outcomes:
In probability theory,
The set is called the sample space.
Each is called an outcome.
A subset is called an event.
Denote by the set of all events.
Probability distributions map events to probabilities,

## Slide 12: Examples
Suppose the probabilities associated with the five outcomes are given as:
Category () | 
Cardboard | 0.20
Paper | 0.30
Cans | 0.25
Scrap Metal | 0.20
Bottle | 0.05
Cardboard | 0.20
Paper | 0.30
Cans | 0.25
Scrap Metal | 0.20
Bottle | 0.05
Define three events
Compute the following:
The probability that an item is a paper product:
The probability that an item is a metal product:
Answers:

## Slide 13: Some properties of probability distributions
Three Axioms of Probability Theory:
For
  There’s no such thing as negative probability.
  The probability that something happened is 1.
For if , then
  If two events are disjoint (aka mutually exclusive), then the probability that one of the two events occurred equals the sum of the probabilities for the two events.
  The second and third axiom immediately imply that

## Slide 14: A handy relationship:
and we can conclude that
which implies
Proof:
implies [Axiom 3]
impies [Axiom 2]
Together, 1 and 2 imply

## Slide 15: Examples
Suppose the probabilities associated with the five outcomes are given as:
Category () | 
Cardboard | 0.20
Paper | 0.30
Cans | 0.25
Scrap Metal | 0.20
Bottle | 0.05
Cardboard | 0.20
Paper | 0.30
Cans | 0.25
Scrap Metal | 0.20
Bottle | 0.05
Define two events
Compute the following:
The probability that an item is a paper product:
The probability that an item is a metal product:
The probability that an item is not a paper product
Answers:
Answers:

## Slide 16: Another handy relationship:
The probability of an event is equal to the sum of the probabilities of its elements:

## Slide 17: Another handy relationship:
The probability of an event is equal to the sum of the probabilities of its elements:
Proof:
Let (can be finite or not)
Define
Base case: []
Hypothesis:
Induction:
  []
  [Axiom 3, since ]
  [Apply Induction]

## Slide 18: Prior Probability Distributions
What can we say about the probabilities of various outcome before we even invoke the robot’s sensors?
Our beliefs about the probabilities of various outcomes can be encoded in a prior distribution --- i.e., the a priori belief about the world.
Priors can be estimated using data, or can be inferred using domain knowledge (e.g., a fair coin should land on heads 50% of the time).
In the book, we estimate prior probabilities using observed data:
Cardboard occurs about 200 times for each 1000 item of trash.
Paper occurs about 300 times for each 1000 item of trash.
Cans occur about 250 times for each 1000 item of trash.
Scrap Metal occurs about 200 times for each 1000 item of trash.
Bottles occur about 50 times for each 1000 item of trash.
Is there any reason to believe that this approach should work in practice?

## Slide 19: Borel’s law of large numbers
Let be an event with probability
Suppose we run our experiment times, and we observe that event occurs times.
Then, with probability one
As the number of trials goes to infinity, the proportion of times that an event occurs approaches the probability of that event.
If we make enough observations, we can start to trust that we have good estimates of prior probabilities!
Shamelessly taken from Wikipedia.

## Slide 20: Machine Learning
In fact, we have just seen a first, simple example of machine learning:
Count the number of occurrences of each category.
Use their relative proportions as an estimate of the prior probability distribution.
We’ll go a bit deeper later in this chapter.

## Slide 21: Simulation by sampling
Often useful to simulate robot systems. In our case, we might like to simulate the arrival of trash to our sorting system, such that it accurately reflects the prior distribution?
How can we generate a sequence of samples, say , such that for approximately 20% of the samples, for approximately 30% of the samples, etc.?
Image from here

## Slide 22: Random Variables
A random variable is a mapping from outcomes to real numbers, .
For example, we can map our categories to integers:
Cardboard 0
Paper 1
Can 2
Scrap Metal 3
Bottle 4
We typically use upper case letters, e.g., , to denote a random variable, and lower-case letters, e.g., , to denote the values taken by .
In our example, indicates that is a random variable that can take values from the set .

## Slide 23: Probability Mass Functions (pmf’s)
When a random variable takes its values from a finite (or possibly countably infinite) set, it is called a discrete random variable.
The probability distribution for a discrete random variable is typically defined as a probability mass function (pmf).
For random variable , the pmf is defined as
For our example,
cardboard
paper
can
scrap metal
bottle
As we will soon see, random variables can be very useful for outcomes that are naturally associated to real numbers, e.g., roll of a die, weight of a person, or, in our case, cost of applying an action.

## Slide 24: Using pmf’s
Even for this example, where categories don’t naturally have numerical semantics, we can use the pmf to answer interesting questions.
For example, what is the probability that an object is a paper product?
Paper products correspond to paper and cardboard,
Alternatively, we could write:
This form, turns out to be very useful.

## Slide 25: Cumulative Distribution Function
The Cumulative Distribution Function (CDF) is defined as
If we order the ’s, such that we can write this as:
when we choose such that .

## Slide 26: CDF for our trash categories
Category () | r.v. | 
Cardboard | 0 | 0.20,
Paper | 1 | 0.50,
Cans | 2 | 0.75,
Scrap Metal | 3 | 0.90,
Bottle | 4 | 1.00,
Cardboard | 0 | 
Paper | 1 | 
Cans | 2 | 
Scrap Metal | 3 | 
Bottle | 4 | 
It is straightforward to compute the CDF for the r.v. associated to various trash categories:
r.v. | 
0 | 0.20
1 | 0.30
2 | 0.25
3 | 0.20
4 | 0.05
0 | 0.20
1 | 0.30
2 | 0.25
3 | 0.20
4 | 0.05

## Slide 27: Simulation by sampling
So, how can we generate a sequence of samples, say , such that for approximately 20% of the samples, for approximately 30% of the samples, etc.?
Sadly, most programming languages do not include library functions to sample from arbitrary probability distributions.
Happily, the is almost always a random number generator that generates a random sample from the unit interval, .
The notation indicates that is a number chosen at random from the interval , and that all possible outcomes are equally likely.
Let’s see how to use this…

## Slide 28: Simulation by sampling
Suppose we generate the samples and
r.v. |  | 
0 | 0.20 | 0.20
1 | 0.30 | 0.50
2 | 0.25 | 0.75
3 | 0.20 | 0.95
4 | 0.05 | 1.00
0 | 0.20 | 0.20
1 | 0.30 | 0.50
2 | 0.25 | 0.75
3 | 0.20 | 0.95
4 | 0.05 | 1.00
Note that
The probability that this occurs is exactly 0.05, since the probability of for the uniform distribution on .
…. Return category bottle.
We can generalize this to develop an algorithm that draws a sample from an arbitrary distribution.
Generate a sample .
Determine such that .
Select category
Similarly,
The probability that this occurs is exactly 0.30.
… Return category paper.

## Slide 29: Use the book!
Now is the time to visit the online book, explore the concepts, and play with the code to ensure that you understand what we have just discussed.
Try different prior distributions, and build the corresponding CDF.
Be sure that your hand calculations match the results from the code.
Generate many samples. Compare the sample distribution (i.e., the proportion of occurrences of each category) to the true prior.
Increase the number of samples. You should notice that the sampling distribution becomes increasingly similar to the true prior as you increase the number of samples.

## Slide 30: Actions
For this problem, the robot either places an item of trash into one of three bins, or lets the item pass through the work cell.
This gives four possible actions:
: Glass Bin
: Metal Bin
: Paper Bin
: Nop (let object pass through the workcell)
For this chapter, we assume that actions are executed without error, every time.
However, since we don’t know with certainty the category for an item of trash in the work cell, the efficacy of an action is also uncertain.

## Slide 31: Assessing Risk
COST | cardboard | paper | can | scrap metal | bottle
glass bin | 2 | 2 | 4 | 6 | 0
metal bin | 1 | 1 | 0 | 0 | 2
paper bin | 0 | 0 | 5 | 10 | 3
nop | 1 | 1 | 1 | 1 | 1
Because there is uncertainty in the category of a piece of trash, the robot risks making mistakes when choosing actions.
Different mistakes have different costs.
  Placing metal in the paper bin might seriously damage paper processing equipment.
  Placing paper in the metal bin is unlikely to cause much harm.
To account for these variations, we can define a table of costs for applying each action (rows) to each category (columns).

## Slide 32: Assessing Risk
COST | cardboard | paper | can | scrap metal | bottle
glass bin | 2 | 2 | 4 | 6 | 0
metal bin | 1 | 1 | 0 | 0 | 2
paper bin | 0 | 0 | 5 | 10 | 3
nop | 1 | 1 | 1 | 1 | 1
Because there is uncertainty in the category of a piece of trash, the robot risks making mistakes when choosing actions.
Different mistakes have different costs.
  Placing metal in the paper bin might seriously damage paper processing equipment.
  Placing paper in the metal bin is unlikely to cause much harm.
We assign zero costs to correct actions.

## Slide 33: Assessing Risk
COST | cardboard | paper | can | scrap metal | bottle
glass bin | 2 | 2 | 4 | 6 | 0
metal bin | 1 | 1 | 0 | 0 | 2
paper bin | 0 | 0 | 5 | 10 | 3
nop | 1 | 1 | 1 | 1 | 1
Because there is uncertainty in the category of a piece of trash, the robot risks making mistakes when choosing actions.
Different mistakes have different costs.
  Placing metal in the paper bin could cause serious damage of paper processing equipment.
  Placing paper in the metal bin is unlikely to cause much harm.
We assign zero costs to correct actions.
The cost of Nop is due to the need for human labor to sort the item of trash.

## Slide 34: Cost as a Random Variable
Since we only have probabilistic knowledge of an item’s category, we can regard the cost of executing an action as a discrete random variable.
Consider action , place the item in the mixed paper bin.
Let be the r.v. that denotes the cost of applying action .
From the table of costs, we see that , since these are the only possible costs for this action.
What can we say about the probability distribution for ?

## Slide 35: Computing pmf’s
To compute the pmf, recall that the random variable is a mapping from outcomes to real numbers.
There are five possible outcomes. The object must be from one of five categories, each of which has a cost.
Compute for each
Category | P(C) | Cost
cardboard | 0.20 | 0
paper | 0.30 | 0
can | 0.25 | 5
scrap metal | 0.20 | 10
bottle | 0.05 | 3
for cardboard and paper.
for can.
for bottle.
for scrap metal.
0

## Slide 36: Expectation
Probabilities tell us something about a single outcome, but this isn’t really very useful. Gamblers who make one-time bets based on probabilities can lose a lot of money.
Most robots operate for prolonged periods of time.
The notion of average cost over many trials seems like a useful thing to know.
This is exactly the concept of expectation in probability theory.

## Slide 37: Expectation
If a r.v. takes its values from a finite set, , the expected value of , denoted , is defined by:
Expectation is a property of a probability distribution
is not the value you should expect to see for any specific outcome!!

## Slide 38: Examples
Let be a discrete r.v. that corresponds to the number of dots shown on a fair die.
and for all
Compute .

## Slide 39: Trash Sorting…
We can now easily evaluate the expected cost for each action under the prior probability distribution.
Expected Cost
3.2
0.6
3.4
1.0
COST | Card board | paper | can | scrap metal | bottle
glass bin | 2 | 2 | 4 | 6 | 0
metal bin | 1 | 1 | 0 | 0 | 2
paper bin | 0 | 0 | 5 | 10 | 3
nop | 1 | 1 | 1 | 1 | 1
 | 0.20 | 0.30 | 0.25 | 0.20 | 0.05
COST | Card board | paper | can | scrap metal | bottle
glass bin | 2 | 2 | 4 | 6 | 0
metal bin | 1 | 1 | 0 | 0 | 2
paper bin | 0 | 0 | 5 | 10 | 3
nop | 1 | 1 | 1 | 1 | 1
 | 0.20 | 0.30 | 0.25 | 0.20 | 0.05
0

## Slide 40: Simulation by sampling
Earlier, we simulated our trash sorting system using a sampling algorithm. Let’s apply those ideas here.
Generate samples from the prior distribution on categories.
Compute the cost for each sample for action .
Compute the average cost as:
Compare to for action (where is the r.v. for cost).

## Slide 41: Probability vs Statistics
Probability theory is the study of a certain class of mathematical functions (probability distributions).
A statistic is any function of data (including the identity function), and statistics is the study of such functions.
is a property of
  Probability Theory
is a function of data,
  Statistics

## Slide 42: Probability Theory and Statistics
If it happens that certain probability distributions do a good job of describing how the world behaves, then probability theory can provide a rigorous basis for a system of inference about data.
The Weak Law of Large Numbers:
Consider a data set drawn from probability distribution , with expected value
For any , if denotes the average of a data set of size , then
As the size of the data set increases, with probability one the average is arbitrarily close to the mean.

## Slide 43: Probability Theory and Statistics
The connections between probability theory and statistics are often formalized by theorems that express variations on a simple concept:
As the size of a data set becomes large, the statistics of that data set will become increasingly good approximations for various properties of the underlying probability distribution from which the data set was generated.
This is one of the reasons simulation by sampling works.
These theorems are important for statistical inference, machine learning, and many other problems that involve data drawn from stochastic systems.

## Slide 44: Next Lecture: Sensing and Perception
Conditional probability:
  How do sensor observations affect our beliefs about the world?
  A key tool for data-based inference
Continuous random variables:
  Unlike our five categories of trash, some things are best described along a continuum.
  Things like weight, distance are described using continuous measurements.
  Gaussian Distributions
Maximum likelihood inference
  Making decisions using conditional probabilities
  Combining information from multiple sensors